## Slide 1: Chapter 5
Telescopes
Copyright © McGraw-Hill Education. Permission required for reproduction or display.

## Slide 2: Tools of the Trade: Telescopes
Stars and other celestial objects are too far away to test directly
  Astronomers passively collect radiation emitted from distant objects
  Extremely faint objects make collection of radiation difficult
Specialized Instruments Required
  Need to measure brightness, spectra, and positions with high precision
  Astronomers use mirrored telescopes and observatories
Modern astronomers are rarely at the eyepiece, more often they are at a computer terminal!

## Slide 3: The Powers of a Telescope
Collecting Power
  Bigger telescope, more light collected!
Focusing Power
  Use mirrors or lenses to bend the path of light rays to create images
Resolving Power
  Picking out the details in an image

## Slide 4: Light Gathering Power
Light collected proportional to “collector” area
  Pupil for the eye
  Mirror or lens for a telescope
Telescope “funnels” light to our eyes for a brighter image
Small changes in “collector” radius give large change in number of photons caught
Telescopes described by lens or mirror diameter

## Slide 5: Focusing Power
Refraction
  Light moving at an angle from one material to another will bend due to a process called refraction
  Refraction occurs because the speed of light is different in different materials

## Slide 6: Refraction

## Slide 7: Refracting Telescopes
A lens employs refraction to bend light
Telescopes that employ lenses to collect and focus light are called refractors

## Slide 8: Disadvantages to Refractors
Lenses have many disadvantages in large telescopes!
  Large lenses are extremely expensive to fabricate
  A large lens will sag in the center since it can only be supported on the edges
  Dispersion causes images to have colored fringes
  Many lens materials absorb short-wavelength light

## Slide 9: Reflecting Telescopes
Reflectors
  Used almost exclusively by astronomers today
  Twin Keck telescopes, located on the 14,000 foot volcanic peak Mauna Kea in Hawaii, have 10-meter collector mirrors!
  Light is focused in front of the mirror

## Slide 10: Mirrors in Reflectors
A secondary mirror may be used to deflect the light to the side or through a hole in the primary mirror
Multi-mirror instruments and extremely thin mirrors are two modern approaches to dealing with large pieces of glass in a telescope system

## Slide 11: Styles of Reflectors

## Slide 12: Resolving Power
A telescope’s ability to discern detail is referred to as its resolving power
Resolving power is limited by the wave nature of light through a phenomenon called diffraction
Waves are diffracted as they pass through narrow openings
A diffracted point source of light appears as a point surrounded by rings of light

## Slide 13: Resolving Power and Aperture
Two points of light separated by an angle a (in arcsec) can be seen at a wavelength l (in nm) only if the telescope diameter D (in cm) satisfies:
  D > 0.02 l/a

## Slide 14: Increasing Resolving Power: Interferometers
  For a given wavelength, resolution is increased for a larger telescope diameter
  An interferometer accomplishes this by simultaneously combining observations from two or more widely-spaced telescopes

## Slide 15: Interferometers
The resolution is determined by the individual telescope separations and not the individual diameters of the telescopes themselves
Key to the process is the wave nature of interference and the electronic processing of the waves from the various telescopes

## Slide 16: Detecting the Light
The Human Eye
  Once used with a telescope to record observations or make sketches
  Not good at detecting faint light, even with the 10-meter Keck telescopes
Photographic Film
  Chemically stores data to increase sensitivity to dim light
  Very inefficient: Only 4% of striking photons recorded on film
Electronic Detectors
  Incoming photons strike an array of semiconductor pixels that are coupled to a computer
  Efficiencies of 75% possible
  CCD (Charged-coupled Device) for pictures

## Slide 17: Charge-Coupled Devices (CCDs)
CCDs are ~20x more sensitive to faint light than photographic film
Incoming light strikes a semiconductor surface, freeing electrons
Number of electrons is proportional to intensity of the light.
Amount of charge liberated is read out to a computer to create an image.

## Slide 18: Nonvisible Wavelengths
Many astronomical objects radiate in wavelengths other visible
  Cold gas clouds radiate in the radio
  Dust clouds radiate in the infrared
  Hot gases around black holes emit x-rays

## Slide 19: Radio Observatories

## Slide 20: Radio Observations
False color images are typically used to depict wavelength distributions in non-visible observations

## Slide 21: Atmospheric Windows

## Slide 22: Major Space Observatories
Why put them in space?

## Slide 23: Space vs. Ground-Based Observatories
Space-Based Advantages
  Freedom from atmospheric blurring
  Freedom of atmospheric absorption
Ground-Based Advantages
  Larger collecting power
  Equipment easily fixed
Ground-Based Considerations
  Weather, humidity, and haze
  Light pollution

## Slide 24: Observatories
The immense telescopes and their associated equipment require observatories to facilitate their use and protection from the elements
Thousands of observatories are scattered throughout the world and are on every continent including Antarctica
Some observatories:
  Twin 10-meter Keck telescopes are largest in U.S.
  The Hobby-Eberly Telescope uses 91 1-meter mirrors set in an 11-meter disk
  Largest optical telescope, VLT (Very Large Telescope) in Chile, is an array of four 8-meter mirrors

## Slide 25: Going Observing
To observe at a major observatory, an astronomer must:
  Submit a proposal to a committee that allocates telescope time
  If given observing time, assure all necessary equipment and materials will be available
  Be prepared to observe at various hours of the day
Astronomers may also “observe” via the Internet
  Large data archives now exist for investigations covering certain wavelengths sometimes for the entire sky
  Archives help better prepare astronomers for onsite observations at an observatory

## Slide 26: Computers and Astronomy
For many astronomers, operating a computer and being able to program are more important than knowing how to use a telescope
Computers accomplish several tasks:
  Solve equations
  Move telescopes and
  feed information to detectors
  Convert data into useful form
  Networks for communication
  and data exchange

## Slide 27: Scintillation
Refraction is also responsible for seeing
  Twinkling of stars
  AKA Scintillation
Temperature and density differences in pockets of air shift the image of the star

## Slide 28: Atmospheric Blurring
  The condition of the sky for viewing is referred to as the seeing
  Distorted seeing can be improved by adaptive optics, which employs a powerful laser and correcting mirrors to offset scintillation
  Many telescopes are built in high-altitude, dry environments to reduce scintillation.

## Slide 29: Light Pollution